## Slide 1
NeuroSurveillance
An open, low-cost, EEG-synchronized video monitoring
system for long circadian recordings
Andrea • Lab Meeting • Friday 2026-04-10

## Slide 2
At a Glance
One-line pitch
• ~$1,174 reproducible 4-chamber system
• Auto-syncs video to NeuroNexus Radiens EEG (software, ~1 s latency)
• 24/7 operation with full monitoring + Slack alerting
• Production-operational as of 2026-04-06
• Open source, fully documented (38+ vault pages)

## Slide 3
§ 1
Current State of the Setup

## Slide 4
Hardware
• 2× Raspberry Pi 5 — 192.168.0.11 and 192.168.0.12
– Each with dual CSI cameras → 4 cameras total
– 1024×768 @ 15 fps, H.264 only
– Waveshare PoE HAT (EEPROM tuned: PSU_MAX_CURRENT=5000, POWER_OFF_ON_HALT=1)
• ASUS NUC 14 Pro — 192.168.0.50
– Intel Core Ultra 5 125H (14 cores), Intel Arc iGPU (QSV)
– 30.6 GB RAM, 1.9 TB NVMe, Ubuntu 24.04
• Synology NAS (long-term storage, Tailscale pending)

## Slide 5
Software Stack
Everything is containerized or systemd-managed
• go2rtc v1.9.14 on each Pi — RTSP streaming via rpicam-vid exec
• Frigate 0.16.1 (Docker) — Intel QSV H.264 hardware decode
• Mosquitto MQTT — recording control broker
• NeuroSurveillance session daemon — Python 3.12 / Flask
• Desktop UI — Tauri v2 + React 19 + TypeScript
• Netdata 2.9.0 + Uptime Kuma — monitoring & alerting

## Slide 6
Hard Rules Learned the Hard Way
Every rule traces back to a specific incident report
• H.264 ONLY — H.265 causes kernel panics on Pi 5
• KillMode=control-group in systemd — prevents zombie rpicam-vid
• rpicam-vid direct exec — no ffmpeg pipes
• apt-mark hold on Docker packages — prevents surprise Frigate restarts
• Always pin Docker image versions

## Slide 7
§ 2
Alerts & Resource Monitoring

## Slide 8
Netdata — 16 Custom NVR Alerts
/etc/netdata/health.d/nvr-alerts.conf
• CPU > 85% / 95% (warn/crit, 10 min avg)
• CPU iowait > 40% (disk bottleneck)
• RAM available < 10% / 5%
• Swap usage > 50%
• Disk space > 90% / 95% per mount
• Disk inodes > 90% / 98%
• Docker container unhealthy / down (Frigate, Mosquitto, Kuma)
• CPU package temperature > 85°C / 95°C
• Hysteresis + 15-min recovery delays → no flapping

## Slide 9
Uptime Kuma — 7 Monitors, Slack Alerting
• go2rtc on Pi 1 (192.168.0.11)
• go2rtc on Pi 2 (192.168.0.12)
• Frigate NVR
• Mosquitto MQTT broker
• NeuroSurveillance session daemon
• Netdata (NVR)
• Uptime Kuma self-check
• Public status page: 192.168.0.50:3001/status/neurosurveillance

## Slide 10
Pi-Side Watchdogs
• Hardware watchdog — systemd RuntimeWatchdogSec=30s (auto-reboots hung Pi)
• Crash-canary script — logs temp, throttle, CPU, RAM every 30 s
– → pre-crash forensics, catches slow-death patterns
• NVR-initiated Pi health check — pi-monitor.sh pings every 2 min
– → catches silent PoE power failures
• systemd Restart=always on go2rtc, session daemon

## Slide 11
Real Incident — 2026-04-02 Thermal Spikes
Why monitoring matters: a concrete example
• Symptom — CPU package 87–92°C, recurring every 35–40 min
• Root cause — allegoserver (Radiens) busy-polling USB → CPU 109%
• Fix — Intel RAPL 20 W power cap via systemd service
• Result — baseline dropped to ~58°C (17°C headroom before alerts)
• → Monitoring caught it; incident report + fix fully documented

## Slide 12
§ 3
Python Session Daemon — Backend & API

## Slide 13
Role
• The glue between NeuroNexus Radiens (EEG) and Frigate (video)
• Runs as systemd service on the NVR
• Flask REST API on 127.0.0.1:8585
• Python 3.12, paho-mqtt, radiens AllegoClient SDK
• Source: private GitHub repo (neurosurveillance)

## Slide 14
Module Architecture
• daemon.py — orchestrator, 1 s poll loop
• radiens_poller.py — detects R_OFF ↔ R_ON via AllegoClient.get_status()
• frigate_controller.py — MQTT ON/OFF + Frigate export API (±2 s buffer)
• session_manager.py — per-chamber state, filenames, JSON sidecars
• manual_session_manager.py — handles Frigate-button recordings
• storage_monitor.py — disk sampling, 200 GB EEG reserve enforcement
• api.py — Flask REST endpoints

## Slide 15
Key Design Decisions
"Why you won't lose data"
• 1. Autonomous core — if daemon crashes mid-session, Frigate keeps rolling
• 2. Metadata optional — missing → 'unknown', no data lost
• 3. Multi-chamber independent state — 4 chambers run in parallel
• 4. Daemon only OBSERVES Radiens — never controls it
• → Researcher stays in charge; system is fail-safe by default

## Slide 16
API Surface
• GET /api/status — full daemon state, sessions, pending metadata
• POST /api/session/metadata?chamber_id=X — set mouse / type / user
• GET /api/session/history — past sessions (Radiens + manual)
• GET /api/health — 200 if Radiens + MQTT connected, else 503
• GET /api/storage — disk usage, can_record flag, EEG reserve
• GET /api/storage/estimate?cameras=N&hours=H — size calculator
• GET /api/storage/camera-bitrates — live from go2rtc on each Pi

## Slide 17
Synchronization
• Method — Radiens AllegoClient polling
• Polling interval — 1 second
• Export timestamp buffer — ±2 seconds (guarantees segment capture)
• Transitions detected — R_OFF → R_ON (start), R_ON → R_OFF (stop + export)
• Good enough for behavior; NOT ms-level (see Section 7)

## Slide 18
§ 4
Desktop GUI — How to Use It

## Slide 19
Stack & Layout
• Tauri v2 + React 19 + TypeScript + Vite
• Tailwind CSS + DaisyUI, dark mode by default
• Window: min 1024×700, default 1400×900
• Components — ChamberSilo, SessionSetup, LiveStatus, CameraPreview,
– StoragePanel, SystemHealth, SessionHistory
• Polling — status 1.5 s · health 5 s · storage 10 s · camera snap 1 s

## Slide 20
User Workflow — Normal Session
Same muscle memory whether you're recording 1 or 4 chambers
• 1. Open the NeuroSurveillance Session Controller
• 2. For each chamber: enter Mouse ID, pick Recording Type, pick your name → Set Metadata
• 3. Start EEG recording in Radiens → video auto-starts on all cameras
• 4. Run the experiment (daemon is silent)
• 5. Stop EEG in Radiens → video auto-stops and exports
• 6. Check Session History panel for completion & file paths

## Slide 21
Manual Override & Settings
• Manual recording — click Record in the Frigate UI
– → daemon detects, inherits pending metadata, 5 s min duration filter
• Settings modal — cameras, recording types, lab members, Frigate URL
– → persisted in localStorage, per-workstation
• Storage badge in header — always visible, green/yellow/red

## Slide 22
§ 5
Storage Management & NAS Transfer

## Slide 23
Directory Layout
• /srv/frigate/storage/recordings — raw Frigate segments
• /srv/frigate/storage/exports — temp Frigate exports
• /srv/frigate/storage/clips — Frigate event clips
• /opt/neurosurveillance/sessions — JSON session sidecars
• /opt/neurosurveillance/exports — organized by user/mouse/date
•
• Example: exports/andrea/HETCF3R1/2026-04-06/2604061430_HETCF3R1_basal.mp4

## Slide 24
Capacity Math
The lab will ask — have the numbers ready
• Per camera: ~1.7 Mbps measured (target 1.5 Mbps + VBR overhead)
• Per camera/day: ~18 GB
• 4 cameras × 24 h: ~72 GB/day
• 7-day retention window: ~504 GB used
• 1.9 TB NVMe → ~26 days of 4-camera headroom
• 200 GB EEG reserve — hard-enforced, recording blocks below it

## Slide 25
StorageMonitor — How It Enforces the Reserve
• Background thread, os.statvfs() every 30 s (single syscall, ~0 ms)
• Atomic dict swap → API thread never reads partial data
• Category scans (exports/recordings/clips) cached 5 min
• can_start_recording() returns False if available < 200 GB
• Bitrate sync button — live-queries go2rtc /api/streams on both Pis
– Parses --bitrate from rpicam-vid exec command

## Slide 26
NAS Transfer — Current State
Being honest about what's done and what's not
• Configured but NOT yet deployed
• Target — Synology NAS at 100.120.86.10
• Blocker — Tailscale VPN setup to NAS
• config.yaml has nas: stub ready to fill in
• Short-term roadmap item (next 2–4 weeks)

## Slide 27
§ 6
Strengths vs. Recent Publications

## Slide 28
How We Compare
System | Cost | EEG Sync | Open Source
NeuroSurveillance (ours) | ~$1,174 | Radiens API, ~1 s, ±2 s buffer | Yes
MouseVUER (2024, Nat. Sci. Rep.) | $2–3k | none | Yes
OpenVEEG (2018) | $5–10k | ms-level, OpenEphys | Partial
Noldus EthoVision | $15–20k | limited | No
Clever Sys HomeCageScan | $10–15k | none | No
SIESTA (2025) | — | ECoG/EMG only, no video | research code

## Slide 29
Novel Contributions
• 1. First open-source Frigate ↔ NeuroNexus Radiens auto-sync (AllegoClient)
• 2. Multi-chamber independent metadata — 4 mice, 4 contexts, one app
• 3. MQTT pub/sub → loose coupling, fail-safe recording
• 4. Full operational documentation — 38+ vault pages incl. incident reports
• 5. ~$1.2 k vs. $5–20 k commercial — fully reproducible

## Slide 30
Key References
All listed in 06-references/progress-meeting-2026-03-12.md
• MouseVUER — Nature Sci. Rep., 2024
• OpenVEEG — PMC, 2018
• SIESTA — PMC, 2025 (ECoG/EMG sleep staging)
• SAGER — Sensors, 2025 (EEG vigilance-state classification)
• Spyglass — eLife, 2024 (reproducible neuroscience data)
• FERAL — bioRxiv, 2025 (video → behavior w/o pose estimation, Rockefeller)
• Lightning Pose — Nature Methods, 2024

## Slide 31
§ 7
Future: Hardware EEG ↔ Video Sync via XDAQ

## Slide 32
Current Sync vs. Planned Upgrade
• Current — software polling via Radiens API
– ~1 s latency, ±2 s export buffer
– Good for behavior; NOT enough for spike-level alignment
• Planned — wire Pi GPIOs to XDAQ digital I/O
– Hardware-triggered frame markers
– Per-frame temporal alignment with EEG/EMG samples
– Unlocks ms-level correlation analyses

## Slide 33
Preparatory Work Already in Place
• 200 GB EEG reserve enforced in storage monitor
• Session daemon architecture is Radiens-agnostic (observer only)
• Frigate export API buffered ±2 s so no edge frames are lost
• Config schema ready to accept hardware sync metadata
• Per-chamber independent state → scales to more headstages

## Slide 34
Validation & Long-Term Plans
• Short term — ffprobe post-export integrity check
– (lesson from 2026-03-06 19 GB MP4 corruption incident)
• Measure actual Radiens R_ON → first Frigate frame latency
• Long-term stability data from multi-day runs
• Longer horizon — PostgreSQL session DB, NWB export → DANDI archive,
– dual-modality (EEG/EMG + FERAL video) sleep scoring pipeline

## Slide 35
§ 8
Why This Matters for Long / Circadian Recordings

## Slide 36
The Failure Mode We're Engineering Against
Frame the stakes first
• Circadian studies = multi-day continuous runs
• A single crash can ruin a week of data
• A silent failure (no alert) is even worse
• → Every design choice optimizes for uptime AND observability

## Slide 37
Stability Features for 24/7 Operation
• Hardware watchdog (RuntimeWatchdogSec=30s) → auto-reboot on hang
• Crash-canary vitals every 30 s → pre-crash forensics
• NVR-initiated Pi ping every 2 min → catches silent PoE death
• apt-mark hold on Docker → no surprise Frigate restarts
• systemd Restart=always on go2rtc, daemon
• Fail-safe video: MQTT recording state persists ON if daemon crashes
• Thermal headroom: RAPL 20 W cap → 17°C margin before alerts

## Slide 38
Track Record
• 30+ day continuous uptime in Feb 2026 MPEG-TS test
• Stable since 2026-02-19 after PMIC/EEPROM hardening
• Thermal regime verified stable since 2026-04-03
• All monitoring alerts currently CLEAR (as of 2026-04-06)
• Storage headroom: ~26 days of 4-camera recording on 1.9 TB NVMe

## Slide 39
§ 9
Roadmap & Next Steps

## Slide 40
Short-Term (2–4 weeks)
• ffprobe post-export validation → prevent silent corruption
• Finish Tailscale NAS transfer deploy
• Confirm apt-mark hold is effective end-to-end

## Slide 41
Medium-Term (1–3 months)
• Automated sleep scoring (EEG/EMG)
– Collaboration with Prof. Kim Daewook's lab
• FERAL video classifier — train on labeled sleep/wake frames
• Video-EEG temporal alignment validation
• PostgreSQL session database → replace JSON sidecars
• Multi-headstage support — independent Radiens per chamber

## Slide 42
Long-Term (3–6 months)
• NWB export format → DANDI archive submission
• Dual-modality sleep scoring pipeline (EEG/EMG + FERAL video)
• System replication guide
• Methods paper — target: J. Neurosci. Methods / HardwareX

## Slide 43
Summary
• Production-operational 4-chamber EEG-synchronized video system
• Fail-safe, fully monitored, fully documented, ~$1,174
• Engineered for multi-day circadian recordings
• Roadmap: ms-level hardware sync + automated sleep scoring
• Code + docs open-sourceable → reproducible methods paper in sight

## Slide 44
Thank you
Questions?
Andrea • Lab Meeting • 2026-04-10